## Slide 1: Getting Started

## Slide 2: Github
All the Arduino programs required for the workshop are on:
https://github.com/GRIETIOTLAB
- Go to GISMO-VI repository
Go to GettingStarted folder

## Slide 3: Hello World
Blinking an LED
Onboard LED connected to pin 2
Create a new project in Arduino
Copy raw content of GISMO6_LED.ino into the file
Compile and name file as LED
Upload onto GISMO-VI board via USB port
Onboard LED

## Slide 4: LED Blink
void setup()
{
pinMode(2 , OUTPUT);
}
void loop()
{
digitalWrite(2 , HIGH);
delay(1000);
digitalWrite(2, LOW);
delay(1000);
}
Digital output

## Slide 5: Hello World
Select ESP32 Arduino -> ESP32 Dev Module as the Board
Select the COM port to which your bard is mapped

## Slide 6: Relay module
ESP32
13

## Slide 7: Relay module
void setup(){
pinMode(13,OUTPUT);
}
void loop(){
digitalWrite(13,HIGH);
delay(2000);
digitalWrite(13,LOW);
delay(2000);
}
Digital output

## Slide 8: Relay module
GISMO-V
Line
Neutral
Normally open (NO) contacts are brought out onto terminal blocks
On relay switching on, the NO contacts will close and the Line circuit will be complete and the bulb will glow

## Slide 9: Buzzer
void setup(){
pinMode(32,OUTPUT);
}
void loop(){
digitalWrite(32,HIGH);
delay(2000);
digitalWrite(32,LOW);
delay(2000);
}

## Slide 10: Magnetic switch
GND
Internal pullup
Mag sw
ESP32
GPIO16

## Slide 11: Magnetic switch
#define magSW 16
void setup() {
pinMode(magSW,INPUT_PULLUP);
Serial.begin(115200);
}
void loop() {
int sw_status;
sw_status = digitalRead(magSW);
if (sw_status)
Serial.println("Switch open");
else
Serial.println("Switch closed");
delay(1000);
}
Digital input

## Slide 12: Serial Communication
GISMO-VI
Program upload
Debugging

## Slide 13: Serial Communication
int count;
void setup() {
Serial.begin(115200);
}
void loop() {
Serial.println(count);
count++;
if(count == 10) count = 0;
delay(1000);
}

## Slide 14
Soil Moisture sensor
Soil Moisture sensor | ESP32 pin
VCC | 3.3V
A0 | GPIO34
D0 | NC
GND | GND
The soil moisture sensor provides a digital as well as a analog output. We will be using the analog output

## Slide 15: Soil Moisture sensor
void setup(){
Serial.begin(115200);
}
void loop(){
int soilmoisture;
soilmoisture = 4095 – analogRead(34);
Serial.println(soilmoisture);
delay(1000);
}
Analog input

## Slide 16: OLED display
OLED: Organic Light Emitting Diode
OLED display pin | ESP32 pin
GND | GND
VCC | 3.3V
SCL | GPIO22
SDA | GPIO21
I2C

## Slide 17: OLED display
Feature | Value
Screen size | 0.96 inches
Internal controller | SSD1306
Color displayed | Blue
Resolution | 64 x 128
VCC | 3.3V
Protocol | I2C

## Slide 18: OLED Display
#include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3C,21,22);
I2C address
SDA,SCL

## Slide 19: OLED Display
void OLEDInit(){
display.init();
display.setFont(ArialMT_Plain_24);
}

## Slide 20: OLED Display
void OLEDUpdate(){
display.clear();
display.drawstring(0,0,”Hello World”);
display.display();
}

## Slide 21: WiFi
ESP32 acts as a station and gets connected to a WiFi router

## Slide 22: WiFi
#include <WiFi.h>
#define WIFI_SSID “xxxxxxxxxxxxxxxxxx”
#define WIFI_PASSWORD “xxxxxxxxxxxxxxxxxxxxxx”
The SSID (Service Set Identifier) is the name of your wireless network, also known as Network ID. This is viewable to anyone with a wireless device within reachable distance of your network. ... The SSID is the name of your wireless network. This is what you will look for when connecting wireless computers and devices.

## Slide 23: WiFi
WiFiInit(){
pinMode(2,OUTPUT);
WiFi.begin(WIFI_SSID,WIFI_PASSWORD);
Serial.print(“Connecting to WiFi”);
while(WiFi.status() != WL_CONNECTED)
{
Serial.print(“.”);
digitalWrite(2,!digitalRead(2);
delay(300);
}
Serial.print(“Connected with IP:”);
Serial.print(WiFi.localIP());
}

## Slide 24: Firebase
#include <FirebaseESP32.h>
#define FIREBASE_HOST “xxxxxxxxxxxxxxxxxxxxxxx”
#define FIREBASE_AUTH “xxxxxxxxxxxxxxxxxxxxxxx”
FirebaseData firebaseData; // Firebase data object

## Slide 25: Firebase
FirebaseInit(){
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.reconnectWiFi(true);
}
FirebaseWrite(){
Firebase.setFloat(FirebaseData, tag,value);
}

## Slide 26: Credentials.h
#define FIREBASE_HOST "xxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxx"
#define WIFI_SSID "xxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxx"
#include <Wire.h>
#include "SSD1306.h"
#include "FirebaseESP32.h"
FirebaseData firebaseData;
SSD1306 display(0x3c, 21, 22);