## Slide 1: Mini Projects
Using GISMO VI

## Slide 2: Environment Monitoring
IOT Lab, ECE Department
Parameter | Range | Accuracy
Ambient Temperature | 0 – 65 degrees C | +/- 1 degrees
Atmospheric Pressure | 300hPa-1100hPa | +/- 1hPa
Altitude |  | 

## Slide 3: BMP280
IOT Lab, ECE Department
BMP280 | ESP32
VCC | 3.3V
GND | GND
SCL | GPIO22
SDA | GPIO21
Interface to ESP32 is via I2C

## Slide 4: BMP280
IOT Lab, ECE Department
This sensor can measure barometric pressure and temperature with very good accuracy. Because pressure changes with altitude we can also use it as an altimeter with ±1 meter accuracy
Accuracy for barometric pressure is ±1 hPa and ±1.0°C for temperature.
Its small dimensions and its low power consumption allow for the implementation in battery-powered devices such as mobile phones, GPS modules or watches.
Interface with microcontroller is via I2C or SPI

## Slide 5: BMP280
IOT Lab, ECE Department
#include <Adafruit_Sensor.h>
#include <Adafruit_BMP280.h>
#define SEALAVELPRESSURE_HPA (1013.25)
Adafruit_BMP280 bmp;
Class

## Slide 6: BMP280
IOT Lab, ECE Department
bmp.begin(BMP280_ADDRESS_ALT,BMP280_CHIPID);
bmp.setSampling(Adafruit_BMP280::MODE_NORMAL,
Adafruit_BMP280::SAMPLING_X2,
Adafruit_BMP280::SAMPLING_X16,
Adafruit_BMP280::MODE_NORMAL)
bmp.readTemperature();
bmp.readPressure();
bmp.readAlititude(1013.25);

## Slide 7: BMP280 Mobile App
IOT Lab, ECE Department

## Slide 8: Credentials.h
#define FIREBASE_HOST “xxx”
#define FIREBASE_AUTH “xxx”
#define WIFI_SSID “xxx"
#define WIFI_PASSWORD “xxx“
#include <Wire.h> // For I2C communication
#include "SSD1306.h" // For OLED Display
#include "FirebaseESP32.h“// For Firebase
FirebaseData firebaseData;
SSD1306 display(0x3c, 21, 22);

## Slide 9: OLED
void OLEDInit(){
display.init();
display.setFont(ArialMT_Plain_16);
}
Font and Font size

## Slide 10: OLED
void displayValues(){
display.clear();
humidity = 0.0;
myString = "";
dtostrf(humidity,5,1,buffer);
myString.concat(buffer);
myString.concat(" %");
display.drawString(64,0,myString);
myString = "";
dtostrf(atPressure,5,1,buffer);
myString.concat(buffer);
display.drawString(0,30,myString);
myString = "";
dtostrf(altitude,5,1,buffer);
myString.concat(buffer);
myString.concat("m");
display.drawString(64,30,myString);
display.display(); }

## Slide 11: WiFi connectivity
void WiFiInit(){
pinMode(2,OUTPUT);
WiFi.begin(WIFI_SSID, WIFI_PASSWORD);
Serial.print("Connecting to Wi-Fi");
while (WiFi.status() != WL_CONNECTED)
{ Serial.print(".");
digitalWrite(2,!digitalRead(2));
delay(300); }
Serial.println(WiFi.localIP());
}

## Slide 12: Firebase
void FirebaseInit(){
Firebase.begin(FIREBASE_HOST, FIREBASE_AUTH);
Firebase.reconnectWiFi(true);
}

## Slide 13: Firebase
void printValues(){
tempC = bmp.readTemperature();
Firebase.setFloat(firebaseData,"IOTLAB/Environment_Monitor/Temperature",tempC);
atPressure=bmp.readPressure()/100.0F;
Firebase.setFloat(firebaseData,"IOTLAB/Environment_Monitor/Pressure",atPressure);
altitude=bmp.readAltitude(SEALEVELPRESSURE_HPA);
Firebase.setFloat(firebaseData,"IOTLAB/Environment_Monitor/Altitude",altitude);
}