## Slide 1: IoT Projects
Using GISMO-VI Board

## Slide 2: IR based Remote Control
Mobile App
Firebase
GISMO-VI
Local
Cloud
Control Modes

## Slide 3: IR Remote Control
IR Receiver Modules
The Remote unit sends a modulated 38KHz IR signal which is demodulated and interpreted by the IR Receiver module. Each key on the Remote has a unique code which will help identify the key

## Slide 4: IR Remote Control
ON button
OFF Button
Local
Remote

## Slide 5: IR Remote Control

## Slide 8: Basic read
#include <IRremoteESP8266.h>
#include <IRrecv.h>
#include <IRutils.h>
const uint16_t kRecvPin = 4;
IRrecv irrecv(kRecvPin);
decode_results results;
irrecv.enableIRIn();
if (irrecv.decode(&results)) {
long btnValue = results.value;
switch(btnValue){
case 16718055:

## Slide 9: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 10: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.getString(firebaseData,”IOTLAB/Motor_Control/Motor_Cmd”,s);
s1 = s.substring(2,s.length()-2);
mc = s1.toInt();

## Slide 11
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(20,0,”MOTOR ON”);
display.display();
I2C address
SDA, SCL

## Slide 12: Real Time Appliance Control
Based on real time start and stop times set via a mobile app and stored in the cloud database, an appliance (such as a heater) will be started and stopped during the slot time
Instead of using hardware for RTC, cloud based NTP (Network Time Protocol) servers are used to get real time
Real time is fetched from the cloud and if it is within the slot time, the appliance is switched on

## Slide 13: Real Time Appliance Control
The Network Time Protocol (NTP) is used by hundreds of millions of computers and devices to synchronize their clocks over the Internet.
The protocol can be used to synchronize all networked devices to Coordinated Universal Time (UTC)
Coordinated Universal Time (UTC) is a world-wide time standard, closely related to GMT (Greenwich Mean Time)
NTP server : pool.ntp.org
UTC+05:30 is an identifier for a time offset from UTC of +05:30. This time is used in India[1] and Sri Lanka.
3] It is five and a half hours ahead of Coordinated Universal Time.

## Slide 14: NTP server
#include <WiFi.h>
#include "time.h"
#include "Credentials.h"
const char* ntpServer = "pool.ntp.org";
const long gmtOffset_sec = 19800;
// 5 hrs 30 minutes offset converted into seconds
//(5x60 + 30) x 60 = 19800

## Slide 15: Fetching time from NTP server
configTime(gmtOffset_sec, daylightOffset_sec, ntpServer);
struct tm timeinfo;
if(!getLocalTime(&timeinfo)){
Serial.println("Failed to obtain time");
return 0; }
hrs = timeinfo.tm_hour;
mins = timeinfo.tm_min;

## Slide 16: Mobile app
Slot start and end time setting in HH:MM format
Real time display. Real time is fetched from cloud and transferred to cloud database
Appliance status: On/Off

## Slide 17: Cloud database

## Slide 18: Mobile App

## Slide 19: WiFi
#define WIFI_SSID "xxxxxxxxxxxxxx"
#define WIFI_PASSWORD "xxxxxxxxxxxxxxxxxxxxxx"
WiFi.begin(SSID,PASSWORD);
while(WiFi.status() != WL_CONNECTED
{
Serial.print(“.”);
delay(300);
}
Serial.println(WiFi.localIP());

## Slide 20: Firebase
#define FIREBASE_HOST "xxxxxxxxxxxxxx"
#define FIREBASE_AUTH "xxxxxxxxxxxxxxxxxxxxxx"
FirebaseData firebaseData;
Firebase.begin(FIREBASE_HOST,FIREBASE_AUTH);
Firebase.setString(firebaseData,”IOTLAB/Appliance_Control/Current_Time”,s);
Firebase.getString(firebaseData,”IOTLAB/Appliance_Control/Start_Time”,s);
Firebase.getString(firebaseData,”IOTLAB/Appliance_Control/Stop_Time”,s);

## Slide 21
OLED display
IOT Lab, ECE Department
# include <Wire.h>
#include “SSD1306.h”
SSD1306 display(0x3c, 21, 22);
display.init();
display.setFont(ArialMT_Plain_16);
display.clear();
display.drawString(0,0,currentTime);
display.drawstring(0,30,startTime);
display.drawstring(80,30,stopTime);
display.drawCircle(60,36,8);
display.display();
I2C address
SDA, SCL

## Slide 22: Biometric based access control
Mobile app with finger print authentication
Authentication status stored in Firebase
GISMO-V reads authentication status and unlocks/locks a solenoid based lock

## Slide 23: Mobile App
Firebase tag : IOTLAB/Lock_Control/Validation_Status

## Slide 24: Home Safety
PIR sensor for intrusion detection
Magnetic switch to detect door/window open status
The status of the two alerts are transferred to Firebase
Mobile app will display the status of the two alerts

## Slide 25: PIR sensor
A passive infrared sensor is an electronic sensor that measures infrared light radiating from objects. PIR sensors mostly used in PIR-based motion detectors. Also, it used in security alarms and automatic lighting applications.
Generally, PIR sensor can detect animal/human movement in a requirement range. PIR is made of a pyroelectric sensor, which is able to detect different levels of infrared radiation. The detector itself does not emit any energy but passively receives it.

## Slide 26: PIR sensor interface
PIR sensor signal | ESP32 pin
GND | GND
OUT | GPIO33
VCC | 5V
#define PIR 33
pinMode(PIR,INPUT);
int pir_status = digitalRead(PIR);
if (pir_status == HIGH) {
Serial.println("Motion detected!");
loopDelay=3000;}
else {
Serial.println("No Motion detected!");
loopDelay = 1000;}
delay(loopDelay);

## Slide 27: Magnetic switch
GND
Internal pullup
Mag sw
ESP32
GPIO16
#define magSW 16
pinMode(magSW,INPUT_PULLUP)
int status = digitalRead(magSW);
If(status == HIGH)
Serial.println(“ Window open”);
else
Serial.println(“Window closed”);

## Slide 28: Firebase tags
IOTLAB/HSS/MagswStatus
IOTLAB/HSSS/PIRSwitch

## Slide 29: Mobile App

## Slide 30: Gesture Recognition
Following gestures will be recognized:
Up to Down
Down to Up
Left to Right
Right to Left
Far to Near
Near to Far

## Slide 31: APDS9960
The APDS-9960 is a multipurpose sensor that can be used for Ambient Light, RGB Sensing, Proximity Sensing, and Gesture Detection.
APDS9960 pin | ESP32 pin
VL | NC
GND | GND
VCC | 3.3V
Serial Data | SDA
Serial Clock | SCL
Interrupt | GPIO23

## Slide 32: APDS9960
Gesture detection utilizes four directional photodiodes to sense reflected IR energy (sourced by the integrated LED) to convert physical motion information (i.e. velocity, direction and distance) to a digital information.
The gesture engine accommodates a wide range of mobile device gesturing requirements: simple UP-DOWN-RIGHT-LEFT gestures or more complex gestures can be accurately sensed.

## Slide 33: APDS9960
#include <Wire.h>
#include <SparkFun_APDS9960.h>
#define APDS9960_INT 23 // Needs to be an interrupt pin
SparkFun_APDS9960 apds = SparkFun_APDS9960();
pinMode(APDS9960_INT, INPUT);
attachInterrupt(APDS9960_INT, interruptRoutine, FALLING);
apds.init();
apds.enableGestureSensor(true);

## Slide 34: APDS9960
void handleGesture() {
if ( apds.isGestureAvailable() ) {
switch ( apds.readGesture() ) {
case DIR_UP:
Serial.println("UP");
break;
………………..
default:
Serial.println("NONE");
}
}

## Slide 35: Heart Beat Detection
The module features the MAX30102 – a modern, integrated pulse oximeter and heart rate sensor IC, from Analog Devices.
It combines two LEDs, a photodetector, optimized optics, and low-noise analog signal processing to detect pulse oximetry (SpO2) and heart rate (HR) signals.

## Slide 36: Heart Beat Detection
MAX30102 signal | ESP32 pin
VIN | 3.3V
SCL | GPIO22(SCL)
SDA | GPIO21(SDA)
INT | NC
IRD | NC
RD | NC
GND | GND

## Slide 37: Heart Beat Detection
The MAX30102 works by shining both lights onto the finger and measuring the amount of reflected light using a photodetector.
The oxygenated hemoglobin (HbO2) in the arterial blood has the characteristic of absorbing IR light.
The redder the blood (the higher the hemoglobin), the more IR light is absorbed.
As the blood is pumped through the finger with each heartbeat, the amount of reflected light changes, creating a changing waveform at the output of the photodetector.
As you continue to shine light and take photodetector readings, you quickly start to get a heart-beat (HR) pulse reading.

## Slide 38
MAX30105 particleSensor;
particleSensor.begin(Wire, I2C_SPEED_FAST)) //Use default I2C port, 400kHz speed
long irValue = particleSensor.getIR();
if (checkForBeat(irValue) == true)
{
long delta = millis() - lastBeat;
lastBeat = millis();
beatsPerMinute = 60 / (delta / 1000.0);
if (beatsPerMinute < 255 && beatsPerMinute > 20)
{
rates[rateSpot++] = (byte)beatsPerMinute; //Store this reading in the array
rateSpot %= RATE_SIZE; //Wrap variable
beatAvg = 0;
for (byte x = 0 ; x < RATE_SIZE ; x++)
beatAvg += rates[x];
beatAvg /= RATE_SIZE;
}
}

## Slide 39: Alarm bell detection and notification
Detection of a specific alarm bell sound
Capture of audio using a MEMS digital microphone INMP441
Performing an FFT on raw audio signal to detect frequency components
Check for presence of specific frequency component corresponding to alarm bell
Post alarm bell detection status(Bell detected/No bell) to cloud
Pull from cloud and display alarm bell detection status on mobile app

## Slide 40: Alarm bell detection and notification
Offline FFT analysis of alarm bell sound in laptop using Friture, a free real-time audio analyzer tool for Windows to get the frequency of the alarm bell sound
Audio capture using the GISMO6 board with a INMP digital microphone
FFT on the captured audio signal and check for the specific alarm bell frequency

## Slide 41: INMP441
The INMP441 is a high performance, low power, digital output, omnidirectional MEMS(microelectromechanical)microphone
The I2S interface allows the INMP441 to be directly connected to digital processors such as ESP32 without the need for an audio codec for use in the system.
The INMP441 has a flat wideband frequency response that results in high definition of natural sound.

## Slide 42: INMP441

## Slide 43: INMP441 - ESP32 interface
INMP441 signal | ESP32 pin
L/R | GND
WS | GPIO27
SCK | GPIO14
GND | GND
VDD | 3.3V
SD | GPIO12

## Slide 44: FFT basics
A Fourier transform converts a signal from a time domain into the frequency domain.
In the frequency domain the signal is represented by a weighted sum of sine and cosine waves.
A fast Fourier transform, or FFT, is a clever way of computing a discrete Fourier transform in Nlog(N) time instead of N2 time, where N is the number of samples
This method can save a huge amount of processing time, especially with real-world signals that can have many thousands or even millions of samples.

## Slide 45: FFT basics
The signal is scanned and the following parameters are important:
The sampling frequency fs of the measuring system (e.g. 48 kHz). This is the average number of samples obtained in one second (samples per second).
The selected number of samples; the blocklength BL. This is always an integer power to the base 2 in the FFT (e.g., 2^10 = 1024 samples)

## Slide 46: FFT Basics
Bandwidth fn This value indicates the theoretical maximum frequency that can be determined by the FFT.
fn = fs / 2
For example at a sampling rate of 48 kHz, frequency components up to 24 kHz can be theoretically determined.
Measurement duration D. The measurement duration is given by the sampling rate fs and the blocklength BL. D = BL / fs. At fs = 48 kHz and BL = 1024, this yields 1024/48000 Hz = 21.33 ms
Frequency resolution df. The frequency resolution indicates the frequency spacing between two measurement results. df = fs / BL
At fs = 48 kHz and BL = 1024, this gives a df of 48000 Hz / 1024 = 46.88 Hz.

## Slide 47: FFT bins
Frequency bins are intervals between samples in frequency domain
For the project, the sampling rate is 22627Hz and the number of samples is 1024
Divide the 22627Hz range into 1024 intervals – 0-22,22-44,44-66 and so on
The door bell frequency used is 738Hz so it will be ( 738/22 = 33.54 ) in 33rd or 34th bin

## Slide 48: I2S protocol
Inter-IC Sound (I2S) bus – a serial link, is developed especially for digital audio. The bus handles only audio data through a simple, 3-line serial bus consisting of:
Serial Clock (SCL)
Word Select (WS)
  WS = 0 (Left Channel)
  WS = 1 (Right Channel)
Serial Data (SDA)
Transmitter INMP441
Receiver ESP32
WS
SCL
SDA
Receiver = Master

## Slide 49: INMP441 – ESP32 interface
Sensor signal | ESP32 pin
L/R | GND
WS | GPIO27
SCK | GPIO14
GND | GND
VDD | 3.3V
SD | GPIO12